## Slide 1
Chapter Outline
CH 7 Passive Devices
<number>
Inductors
Basic Structure
Inductance Equations
Parasitic Capacitance
Loss Mechanisms
Inductor Modeling
Inductor Structures
Symmetric Inductors
Effect of Ground Shield
Stacked Spirals
Transformers
Structures
Effect of Coupling Capacitance
Transformer Modeling
Varactors
PN Junctions
MOS Varactors
Varactor Modeling

## Slide 2
Motivation for On-Chip Integrated Inductors
CH 7 Passive Devices
<number>
The bond wires and package pins connecting chip to outside world may experience significant coupling
Reduction of off chip components ---> Reduction of system cost.
Modeling issues of off-chip inductors

## Slide 3
Basic Inductor Structure
CH 7 Passive Devices
<number>
Has mutual coupling between every two turns.
Larger inductance than straight wire.
Spiral is implemented on top metal layer to minimize parasitic resistance and capacitance.

## Slide 4
Inductance of N Turn Spiral Structure
CH 7 Passive Devices
<number>
Inductance of an N-turn planar spiral structure inductor has
terms.
Factors that limit the growth rate of an inductance of spiral inductor as function of N:
a) Due to planar geometry the inner turns have smaller size and exhibit smaller inductance.
b) The mutual coupling factor is about 0.7 for adjacent turns hence contributing to lower inductance.

## Slide 5
Geometry of Inductor Effects Inductance
CH 7 Passive Devices
<number>
A two dimensional square spiral inductor is fully specified by following four quantities:
a) Outer dimension, Dout
b) Line width, W
c) Line spacing, S
d) Number of turns, N
Various dimensions of
spiral inductor

## Slide 6
CH 7 Passive Devices
<number>
Doubling the width inevitably decreases the diameter of inner turn, thus lowering their inductance.
The spacing between the legs reduces, hence their mutual inductance also decrease.
Effect of doubling the line width of inductor
Effect of Doubling Line Width of Inductor

## Slide 7
CH 7 Passive Devices
<number>
Obtained from electromagnetic field simulations.
Coupling factor b/w 2 straight metal lines as a function of their normalized spacing
Magnetic Coupling Factor Plot

## Slide 8
CH 7 Passive Devices
<number>
Inductor Structures Encountered in RFIC Design
Octagonal
Symmetric
Stacked
With Grounded shield
Parallel Spirals
Circular
Various inductor geometries shown above are result of improving the trade-offs in inductor design, specifically those between:
The quality factor and the capacitance.
The inductance and the dimensions.
Note → These various inductor geometries provide additional degrees of freedom but also complicate the modeling task.

## Slide 9
CH 7 Passive Devices
<number>
Inductance Equations
Closed form inductance equations can be found based on
1) Curve fitting methods
2) Physical properties of inductors
Various expressions have been reported in literature [1,2,3].
The equation above is an empirical formula which estimates inductance of 5nH to 50nH square spiral inductor within 10% error.
Am – Metal area , Atot – Total Inductor area

## Slide 10
CH 7 Passive Devices
<number>
Parasitic Capacitance of Integrated Inductors
Planar spiral inductor suffers from parasitic capacitance because the metal lines of the inductor exhibit parallel plate capacitance and adjacent turns bear fring capacitance.
Bottom-Plate capacitance
interwinding capacitances

## Slide 11
CH 7 Passive Devices
<number>
Estimation of Parasitic Capacitance
Model of inductor's distributed capacitance to ground
To simplify the analysis we make two assumptions:
1) Each two inductor segments have a mutual coupling of M
2) The coupling is strong enough that M can be assumed approximately equal to Lu
Voltage across each inductor segment:

## Slide 12
CH 7 Passive Devices
<number>
Estimation of Parasitic Capacitance
Capacitance = Ctot /3
If M = Lu , then
Electrical energy stored in node capacitance is:
Total energy stored on all of the unit capacitances =
If k-->infinity and Cu-->0 such that kCu is equal to total wire capacitance:

## Slide 13
CH 7 Passive Devices
<number>
Loss Mechanisms: Metal Resistance
Metal resistance Rs of spiral inductor of inductance L1
Q = Quality factor of inductor
(measure of loss in inductor)

## Slide 14
CH 7 Passive Devices
<number>
Loss Mechanisms: Skin Effect
Current distribution in a conductor at
(a) Low frequency (b) High frequency
Skin depth =
Extra resistance =

## Slide 15
CH 7 Passive Devices
<number>
Skin Effect: Current Crowding Effect
(a) Current distribution in adjacent turns (b) Detailed view of (a)
At fcrit , the magnetic field produced by adjacent turn induces
eddy current, causing unequal distribution of current across the
conductor width, hence altering the effective resistance of the turn.
Based on the observation in [7,8] derive the following expressions:

## Slide 16
CH 7 Passive Devices
<number>
Current Crowding Effect on Parasitic Capacitance
As current flows through a smaller width of conductor, this causes a reduction in the effective area between the metal and substrate, hence there is a reduction in the total capacitance.

## Slide 17
CH 7 Passive Devices
<number>
Capacitive Coupling to Substrate
Substrate loss due to capacitive coupling
Voltage at each point of the spiral rise and fall with time causing displacement current flow between this capacitance and substrate.
This current causes loss and reduces the Q of the inductor.

## Slide 18
CH 7 Passive Devices
<number>
Recap of Basic Electromagnetic Laws
Lenz's Law: States that the current induced by a magnetic field generates another magnetic field opposing the first field.
Faraday's Law: States that a time varying magnetic field induces a voltage and hence a current, if a voltage appears across a conducting material.
Ampere's Law: States that the current flowing through a conductor generates a magnetic field around the conductor.

## Slide 19
CH 7 Passive Devices
<number>
Magnetic Coupling to Substrate
The time varying inductor current generates eddy current in the substrate.
Lenz's law states that this current flows in the opposite direction.
The induction of eddy currents in the substrate can be viewed as transformer coupling.

## Slide 20
CH 7 Passive Devices
<number>
Modeling of Magnetic Coupling by Transformer
Vin = L1sIin + MsI2
-Rsub I2 = L2I2s + MsIin

## Slide 21
CH 7 Passive Devices
<number>
Modeling Loss by Series or Parallel Resistor
A constant series resistance Rs model inductor loss for limited range of frequencies.
A constant parallel resistance Rp model inductor loss for narrow range of frequencies.
Note --> The behavior of Q of inductor predicted by above two models has suggested opposite trends of Q with frequency.
Q = L1 ω/Rs
Q = Rp /L1 ω

## Slide 22
CH 7 Passive Devices
<number>
Modeling Loss by Both Series and Parallel Resistors
Resulting behavior of Q
Modeling loss by both parallel and series resistances
Overall Q of inductor

## Slide 23
CH 7 Passive Devices
<number>
Broadband Model of Inductor
Broadband skin effect model
Broadband model
At low frequencies current is uniformly distributed thorough the conductor and model reduces to R1||R2||.....||Rn [9]
As frequency increases the current moves away from the center of the conductor, as modeled by rising impedance of inductors in each branch.
In [9], a constant ratio of Rj/Rj+1 is maintained to simplify the model. ( Lj and Rj represents the impedance of cylinder j of conductor shown above)

## Slide 24
CH 7 Passive Devices
<number>
Definitions of Q
Reduce any resonant network to a parallel RLC tank,
Lumping all of the loss in a single parallel resistance Rp.
Define

## Slide 25
CH 7 Passive Devices
<number>
Symmetric Inductor
Differential circuits can employ a single symmetric inductor instead of two asymmetric inductors. It has two advantages:
1) Save area
2) Differential geometry also exhibit higher Q.

## Slide 26
CH 7 Passive Devices
<number>
Equivalent Lumped Interwinding Capacitance
a) 3 turn symmetrical inductor (b) equivalent structure (c) Voltage profile
We unwind the structure as depicted above, assuming, an approximation, that all unit inductances are equal and so are all unit capacitances.

## Slide 27
CH 7 Passive Devices
<number>
Equivalent Lumped Interwinding Capacitance
Equivalent lumped interwiding capacitance of a symmetrical inductor is typically much larger than capacitance of substrate, dominating self resonance frequency.
Total energy stored on the four capacitors is =
where C1= C2 = C3 = C4 .Denoting C1+ C2 + C3 + C4 = Ctot , we have
And hence equivalent lumped capacitance is:

## Slide 28
CH 7 Passive Devices
<number>
Mirror/Step Symmetry of Single Ended Inductor
Leq = L1 + L2 – 2M
Lower Q
Load inductors in a diff. pair with
(a) Mirror symmetry (b) Step symmetry
Leq= L1 + L2 + 2M
Higher Q

## Slide 29
CH 7 Passive Devices
<number>
Magnetic Coupling Along Axis of Symmetry
Differential spiral inductor produces a magnetic field on axis of symmetry.
No such coupling in case of two single ended inductors on axis of symmetry
(a) Single-ended inductor (b) Symmetric inductor

## Slide 30
CH 7 Passive Devices
<number>
Example: Inductor with Reduced Magnetic Coupling Along Axis of Symmetry
The structure is more symmetric than single-ended spirals with step symmetry.
Magnetic field of two halves cancel on axis of symmetry
Have lower Q than differential inductor because each half experiences its own substrate losses.

## Slide 31
CH 7 Passive Devices
<number>
Inductors with Ground Shield
This structure allows the displacement current to flow through the low resistance path to ground to avoid electrical loss through substrate.
Eddy currents through a continuous shield drastically reduce inductance and Q, so a “patterned” shield is used.
This shield reduces the effect of capacitive coupling to substrate
Eddy currents of magnetic coupling still flows through substrate.

## Slide 32
CH 7 Passive Devices
<number>
Stacked Inductors
Ltot = L1 + L2 + 2M M = L1 = L2
Ltot = 4L
Similarly, N stacked spiral inductor operating in series raises total inductance by a factor of N2.

## Slide 33
CH 7 Passive Devices
<number>
Equivalent Capacitance for a Stacked Inductor
In addition to substrate and interwinding capacitance it also contains another capacitance in between stacked spirals.
Cm = inner spiral capacitances

## Slide 34
CH 7 Passive Devices
<number>
Transformers
Useful function of transformer in RF Design
Impedance matching
Feedback and feedforward with positive and negative polarity
Single ended to differential conversion and vice-verse.
AC coupling between stages

## Slide 35
CH 7 Passive Devices
<number>
Characteristics of Well-Designed Transformers
Low series resistance in primary and secondary windings.
High magnetic coupling between primary and secondary windings.
Low capacitive coupling between primary and secondary windings.
Low parasitic capacitance to the substrate

## Slide 36
CH 7 Passive Devices
<number>
Transformer Structures
Segments AB and CD are mutually coupled inductors.
Primary and secondary are identical so this is 1:1 transformer.
Transformer derived from a symmetric inductor

## Slide 37
CH 7 Passive Devices
<number>
Simple Transformer Model and its Transfer Function
The transformer action gives
Solve above two equations for I2

## Slide 38
CH 7 Passive Devices
<number>
Simple Transformer Model and its Transfer Function
KCL at output node yields
Replacing I2 in above equation and simplifying the result, we obtain

## Slide 39
CH 7 Passive Devices
<number>
Input Impedance of Transformer Model with CF=0
Setting CF = 0 in above equation
Input Impedance =
Input/output transfer function =

## Slide 40
CH 7 Passive Devices
<number>
Transformer with Turn Ratio More than Unity
Weaker mutual coupling factor
Stronger mutual coupling factor

## Slide 41
CH 7 Passive Devices
<number>
Stacked Transformers
One to One Stack transformer
One to two Stack transformer
Staggering of turns to reduce capacitive coupling
Higher magnetic coupling.
Unlike planar structures, primary and secondary can be identical and symmetrical.
Overall area is less than planar structure
Larger capacitive coupling compared to planar structure.

## Slide 42
CH 7 Passive Devices
<number>
Effect of Coupling Capacitance
For M>0, frequency response exhibit notch at ω Hz.
For M<0, no such notch exist and transformer can work at higher frequency.
So “non-inverting” transformer suffers from lower speed than “inverting” transformer.
Transfer function of transformer at s = jω:

## Slide 43
CH 7 Passive Devices
<number>
Transformer Modeling
Due to the complexity of this model it is very difficult to find the values of each component from measurement or field simulations.

## Slide 44
CH 7 Passive Devices
<number>
T-Line as Inductor
T-Line having short circuit termination act as an inductor (if T-line is much smaller than the wavelength of signal).
T-Line serving as load inductor

## Slide 45
CH 7 Passive Devices
<number>
T-Line as Impedance Transformer
T-Line of length d, terminated with a load impedance of ZL exhibit input impedance = Zin(d).
, Z0 = Characteristic impedance
Example at d= λ/4 then
i.e. a capacitive load transforms to inductive component.
β=2π/λ

## Slide 46
CH 7 Passive Devices
<number>
T-Line Structures: Microstrip
In microstrip structure, signal line realized in top-most metal layer and ground plane is in lower metal layer. Hence have minimum interaction between signal line and substrate.

## Slide 47
CH 7 Passive Devices
<number>
Characteristic Impedance of Micristrips
Note -> Above equation predict characteristic impedance with a large error (as large as 10%).
Characteristic impedance of microstrip, of signal line thickness 't' and height 'h' with respect to ground plane, is.

## Slide 48
CH 7 Passive Devices
<number>
'Q' of Lossy T-Line

## Slide 49
CH 7 Passive Devices
<number>
T-Line Structures: Coplanar Lines
The characteristic impedance of the coplanar structure is higher than that of the microstrip because
1) Thickness of signal and ground lines are quite small, leading to lower capacitance.
2) Spacing between two lines can be small, further decreasing the capacitance.

## Slide 50
CH 7 Passive Devices
<number>
T-Line Structures: Stripline
Stripline structure consists of a signal line surrounded by ground planes.
It produces very little field leakage to surroundings.
The characteristic impedance of the stripline is smaller than both microstrip and coplanar structures.

## Slide 51
CH 7 Passive Devices
<number>
Varactors
Varactor is a voltage-dependent capacitor.
Two important attributes of varactor design become critical in oscillator design
The capacitance range i.e. ratio of maximum to minimum capacitance that varactor can provide.
The quality factor of the varactor.

## Slide 52
CH 7 Passive Devices
<number>
PN Junction Varactor
Varactor capacitance of reversed-biased PN junction.
Cjo = Capacitance at zero bias
Vo = Built-in potential.
m = exponent around 0.3 in integrated structure
Note - Weak dependance of Cj upon Vd, because
(Vd,max = 1V ) Cj,max/Cj,min ~ 1.23 (Low range) .

## Slide 53
CH 7 Passive Devices
<number>
Varactor Q Calculation Issues
As shown above, due to the two dimensional flow of current it is difficult to compute the equivalent series resistance of the structure.
N-well sheet resistance can not be directly applied to calculation of varactor series resistance.
Q of varactor is obtained by measurement on fabricated structure
Difficult to calculate it
Current distribution in varactor

## Slide 54
CH 7 Passive Devices
<number>
MOS Varactor ?
A regular MOSFET exhibits a voltage dependent gate capacitance
The non-monotonic behavior with respect to gate voltage limits the design flexibility.
Variation of gate capacitance with Vgs
Regular MOS device:

## Slide 55
CH 7 Passive Devices
<number>
Accumulation Mode MOS Varactor
Accumulation-mode MOS varactor is obtained by placing an NMOS inside an nwell .
The variation of capacitance with Vgs is monotonic.
The C/V characteristics scale well with scaling in technology.
Unlike PN junction varactor this structure can operate with positive and negative bias so as to provide maximum tuning range.
C/V characteristics of varactor

## Slide 56
CH 7 Passive Devices
<number>
Accumulation Mode MOS Varactor Operation
Vg < Vs
Depletion region is formed under gate oxide.
Equivalent capacitance is the series combination of gate capacitance and depletion capacitance.
Vg > Vs
Formation of channel under gate oxide.

## Slide 57
CH 7 Passive Devices
<number>
Accumulation Mode MOS Varactor: Curve Fitting Model
Here, “Vo” and “a” allow fitting for the slope and the intercept.
Curve fitting model:
The above varactor model translates to different characteristics in different circuit simulators.
Simulation tools (HSPICE) that analyze circuits in terms of voltages and currents interpret the above non-linear capacitance equation correctly.

## Slide 58
CH 7 Passive Devices
<number>
Accumulation Mode MOS Varactor: Charge Equation Model
Charge equation model:
Simulation tools ( Cadence Spectre) that represent the behavior of capacitors by charge equations interpret this charge equation model correctly.

## Slide 59
CH 7 Passive Devices
<number>
Q of Accumulation mode MOS Varactor
Q of varactor:
Determined by the resistance between source and drain terminals.
Approximately calculated by lumped model shown in above.

## Slide 60
CH 7 Passive Devices
<number>
Calculation of Equivalent Resistance and Capacitance Value in Lumped Model.
`
Distributed Model
Equivalent structure for half circuit
Canonical T-line Structure
The equivalent structure above resembles a transmission line consisting of series resistances and parallel capacitances. For general T-line structure the input impedance is :

## Slide 61
CH 7 Passive Devices
<number>
Calculation of Equivalent Resistance and Capacitance Value in Lumped Model
Where Z1 and Y1 are specified for unit length and d is the length of line and from above equivalent structure Z1d=Rtot and Y1d=sCtot.
At frequencies well below 1/(RtotCtot /4), the argument of tanh is much less than unity, allowing the approximation,
It follows that
The lumped model of half of the structure consists of its distributed capacitance in series with 1/3 of its distributed resistance. Accounting for the gray half in equivalent circuit of half structure, we obtain
tanh  =  – 3/3
=  /(1+  2/3)

## Slide 62
CH 7 Passive Devices
<number>
Variation of MOS Varactor Q with Capacitance
Variation of varactor Q with capacitance
For Cmin, the capacitance is small and resistance is large.
For Cmax, the capacitance is large and resistance is small.
Above comments suggest that Q remains relatively constant.
In practice, Q drops as we increase cap from Cmin to Cmax, suggesting that relative rise in capacitance is greater than fall in resistance.

## Slide 63
CH 7 Passive Devices
<number>
Effect of Overlap Capacitance on Capacitance Range
Overlap capacitance is relatively voltage independent.
Overlap capacitance shifts the C/V characteristics up, yielding a ratio of
(Cmax + 2WCov)/(Cmin + 2WCov)

## Slide 64
CH 7 Passive Devices
<number>
Constant Capacitors
RF circuits employ constant capacitors for various purposes:
To adjust the resonance frequency of LC tanks.
To provide coupling between stages.
To bypass the supply rail to ground.
Critical parameters of capacitors used in RF IC design:
Capacitance density.
Parasitic capacitance.
Q of the capacitor.

## Slide 65
CH 7 Passive Devices
<number>
MOS Capacitor: Usage Examples
MOS capacitor used as coupling device.
MOS capacitor used as bypass capacitor

## Slide 66
CH 7 Passive Devices
<number>
MOS Capacitor: Layout
MOS capacitor realized as
multiple short fingers having
resistance:
MOS capacitor realized as
one long finger having resistance

## Slide 67
CH 7 Passive Devices
<number>
Metal Plate Capacitor
Parallel plate capacitor.
This structure employs planes in different metal layers.

## Slide 68
CH 7 Passive Devices
<number>
Metal Plate Capacitor: Bottom Plate Parasitic
Parallel plate capacitor geometry suffers from bottom plate parasitic capacitance.
This capacitance reaches upto 10% of actual capacitance, leading to serious difficulty in circuit design

## Slide 69
CH 7 Passive Devices
<number>
Fringe Capacitor
Fringe capacitor consists of narrow metal lines with minimum spacing.
The lateral electric field between adjacent metal lines leads to a high capacitance density.

## Slide 70
CH 7 Passive Devices
<number>
References

## Slide 71
CH 7 Passive Devices
<number>
References

## Slide 72
CH 7 Passive Devices
<number>
References